Long theoretical questions – Question 4 (reserve) solution & points

Max 30 points

Stating that the body radiates losing thermal energy	3

Determining the thermal energy of the body
The specific heat capacity of an ideal gas is	4
size 12{c rSub { size 8{V} } ="12,5"J cdot K rSup { size 8{ - 1} } cdot ital "mol" rSup { size 8{ - 1} } } {}
or
size 12{c rSub { size 8{p} } ="21"J cdot K rSup { size 8{ - 1} } cdot ital "mol" rSup { size 8{ - 1} } } {}
Both are reasonable as this is an estimate.
10 Jupiter masses is size 12{2 cdot "10" rSup { size 8{"28"} } ital "kg=""10" rSup { size 8{"31"} } ital "mol"} {}	4
Amount of energy corresponding to a change of size 12{ ital "ΔT"} {} will be
size 12{ ital "ΔE=m" cdot c cdot ital "ΔT"} {}	4

Calculation of energy lost through radiation
From the mass and density we calculate radius
size 12{ ital "R=" nroot {3} { { {3 cdot m} over {"4π" cdot ϱ} } } } {} = size 12{"1,69" cdot "10" rSup { size 8{8} } } {} m.	3
Radiated power is thus
size 12{ ital "ΔM=""4π" cdot R rSup { size 8{2} } cdot σ cdot T rSup { size 8{4} } } {}	3
and therefore energy

size 12{ ital "ΔE=""4π" cdot R rSup { size 8{2} } cdot σ cdot T rSup { size 8{4} } cdot ital "Δt"} {}	3
comparing thermal energy and energy loss rate to get ∆t
size 12{ ital "Δt=" { { left (m cdot c cdot ital "ΔT" right )} over {"4π" cdot R rSup { size 8{2} } cdot σ cdot T rSup { size 8{4} } } } } {}	3

The rate of cooling can be therefore calculated as
size 12{ { { ital "ΔT"} over { ital "Δt"} } = { {4 ital "πR" rSup { size 8{2} } ital "σT" rSup { size 8{4} } } over { ital "mc"} } } {}	1
Subsitituting we get about size 12{3 cdot "10" rSup { size 8{4} } } {} years / K, (so quite quickly).	2